## Slide 1
CS 211 · RECITATION 03
Floating point numbers
Build and decode numbers in a small floating point format. We will work through the bits before worrying about implementation.
Today’s path
Binary fractions
Exponent and significand fields
Quiz review: −1.0
Normal and subnormal values
Practice with ratios and bit patterns
HW3 preview
Every example uses a tiny format so every bit has a visible job.
01 / 24
Notes: Suggested 50-minute pacing: binary place values and fields 7 min; normal values 10 min; quiz review 4 min; subnormals and the boundary 12 min; decoding and encoding practice 7 min; rounding and spacing 3 min; HW3 preview and recap 7 min. Pause after the quiz question before revealing the answer. The HW3 details are based on the professor’s description supplied by the TA; the assignment is not officially posted. Source: lecture 6 and the quiz screenshot supplied by the TA.

## Slide 2
FLOATING POINT · FORMAT
A float has three fields
The sign says positive or negative. The exponent sets the scale. The significand carries the detail.
For our nonnegative examples, the sign bit is always 0.
Practice format
S | EEE | FFF
0 | 011 | 010
1 sign bit, 3 exponent bits,
3 stored significand (fraction) bits
Normal values also have a leading 1 that is implied rather than stored.
02 / 24
Notes: The planned assignment accepts exponent-bit count, bias, significand-bit count, numerator, and denominator. Do not present this as the released homework. Explain that these are stored fields, not decimal digits. Here F means the integer represented by the three fraction bits. Lecture 6 reviews normal and subnormal equations.

## Slide 3
FLOATING POINT · PLACE VALUES
Binary fractions use halves
Digits after a binary point are worth 1/2, 1/4, 1/8, and so on. A zero means that place contributes nothing.
Add the places marked 1 to find the value.
0.101₂
1 × 1/2 = 1/2
0 × 1/4 = 0
1 × 1/8 = 1/8
Total = 5/8
Ask students to read 0.011₂ aloud as 1/4 + 1/8 = 3/8.
03 / 24
Notes: Draw place-value columns before introducing exponent fields. This bridges base-2 arithmetic to the 5/4 and 3/16 examples. The 0.101₂ example equals 0.625.

## Slide 4
FLOATING POINT · FIRST STEP
Write a ratio in binary
Start with the value, before thinking about fields.
5/4 is 1.25 in decimal. The quarter is 2⁻², so 5/4 is 1.01 in binary.
5/4 = 1 + 1/4
= 1 + 2⁻²
= 1.01₂
With 3 fraction bits: 1.010₂
Binary places after the point are 1/2, 1/4, 1/8, and so on.
04 / 24
Notes: Draw place-value columns 1, 1/2, 1/4, 1/8. 1.010 binary is exactly 1.25. The trailing zero pads the practice format; it does not change the value. The examples are constructed for teaching, not copied from the unreleased solution.

## Slide 5
FLOATING POINT · NORMAL VALUES
Stored and true exponents
Here E is the unsigned number stored in the exponent bits. Lowercase e is the true exponent in 2ᵉ. For normal values, subtract the bias when decoding and add it when encoding.
Practice bias = 3
Decode bits 001₂:
E = 1 → e = 1 − 3 = −2
Encode true exponent e = −2:
E = −2 + 3 = 1 → bits 001
Symbols vary by source: first decide which exponent is stored.
05 / 24
Notes: State the notation before either formula: this deck uses E for the stored unsigned field and e for the unbiased true exponent. Thus decode e=E−bias; encode E=e+bias. A student may have seen E=e−bias where their E means true exponent. Both describe the same operation with different names. Normal fields have stored E from 1 through 6 in this toy format. E=0 is for zero/subnormals and E=7 is reserved. The planned homework supplies the bias explicitly.

## Slide 6
FLOATING POINT · WORKED EXAMPLE
Encode a normal value: 5/4
5/4 = 1.010₂ × 2⁰.
The true exponent is e = 0, so stored E = 0 + 3 = 3. The fraction after the leading 1 is 010₂, or F = 2.
S = 0
E = 3 = 011₂
F = 2 = 010₂
Fields: 0 | 011 | 010
Check: (1 + 2/8) × 2⁰ = 5/4
The stored fraction has three bits; the implied leading 1 is not one of them.
06 / 24
Notes: Work through this slowly on the board. Ask which part of 1.010 is stored: 010. The lecture equation is (−1)^S × 2^(E−bias) × (1+F/2^sig_bits). For E=3, bias=3, F=2, sig_bits=3 the result is exactly 1.25.

## Slide 7
FLOATING POINT · WORKED EXAMPLE
Decode a normal bit pattern
Read the exponent field as an unsigned integer, then subtract the bias. Read the fraction field as F/8.
Because E is not zero, include the implied leading 1.
Bits: 0 | 010 | 101
E = 2, so e = 2 − 3 = −1
F = 5, so 1 + F/8 = 13/8
Value = (13/8) × 2⁻¹ = 13/16
The bit pattern is a recipe for a value, not the digits of that value.
07 / 24
Notes: Pause at each field and ask students what it means. The sign is zero. E=2 lies in the normal range, e=-1, and F=5. The value is 0.8125.

## Slide 8
FLOATING POINT · QUIZ REVIEW
Quiz review: −1.0 in 8 bits
An 8-bit format has 1 sign bit, 5 exponent bits, 2 stored significand bits, and bias 15. An exponent field of 11111₂ is reserved for infinity and NaN. What representable value is closest to −1.0?
Write each answer in decimal:
value = ?
sign = ?
exponent = ?
significand = ?
Work out the fields before revealing the answer.
08 / 24
Notes: This is adapted from the quiz screenshot supplied by the TA. Give students one or two minutes. The question asks for the closest representable value and the decimal values of the sign, exponent, and significand fields. It is an exact case, so no rounding is needed. Keep the answer hidden until the next slide. The quiz calls the two stored fraction bits significand bits.

## Slide 9
FLOATING POINT · WORKED ANSWER
Quiz answer: −1.0 is exact
−1.0 is representable exactly. Its magnitude is 1.00₂ × 2⁰, so the sign is 1, the true exponent is 0, and the stored fraction is 00₂. Add bias 15 to encode the exponent field.
value = −1.0
sign = 1
exponent = 15
significand = 0
Bits: 1 | 01111 | 00
Check: −(1 + 0/4) × 2^(15−15) = −1
E = 15 is valid; all five exponent bits set would be E = 31.
09 / 24
Notes: Quiz screenshot supplied by the TA. Decode the fields aloud: sign bit 1 makes the value negative; 01111₂ is 15, so true exponent 15−15=0; 00₂ is stored significand field 0, with implied leading 1 for a normal value. Thus (−1)^1 × (1+0/4) × 2^0=−1.0. The reserved all-ones exponent is 11111₂=31, not 01111₂=15. Explicitly tell students that an exact target is its own closest representable value.

## Slide 10
FLOATING POINT · WHY SUBNORMALS
The smallest normal is 1/4
The smallest normal exponent field is E = 1. With bias 3, that means e = −2. If the stored fraction is 000, the value is 1/4. We need another way to represent smaller positive values such as 1/8.
Smallest normal
E = 001₂ → e = 1 − 3 = −2
F = 000₂ → significand 1.000₂
value = 1.000₂ × 2⁻² = 1/4
1/8 is smaller. E = 0 marks a new case.
For E = 0, use the subnormal rule instead of subtracting the bias.
10 / 24
Notes: Pause before giving the subnormal rule. Ask: if E=1 is the smallest normal field, where could 1/8 go? A normal encoding would need true exponent −3 and stored E=0, but zero is reserved for a different rule. The next slide explains that rule using binary digits rather than a formula first. Source: lecture 6 normal and subnormal equations.

## Slide 11
FLOATING POINT · SUBNORMAL RULE
E = 0 drops the hidden 1
Normal values start with an implied 1 before the fraction bits. When E = 0, use an implied 0 instead. Keep the same 2⁻² scale as the smallest normal so the values grow smoothly from zero.
Fixed e = 1 − bias = −2
Normal, E = 1:
1.FFF₂ × 2⁻²
Subnormal, E = 0:
0.FFF₂ × 2⁻²
F = 000 → 0.000₂ × 2⁻² = 0
F = 100 → 0.100₂ × 2⁻² = 1/8
The leading 0 or 1 is implied; only FFF is stored.
11 / 24
Notes: Use the same scale before and after the boundary: 2^(1−bias)=2^-2. This is the key change: replace the normal hidden 1 with 0. Do not compute 0−bias for E=0. Ask students why 0.100 binary is 1/2, then multiply by 1/4 to get 1/8. Source: lecture 6 subnormal equation.

## Slide 12
FLOATING POINT · PLACE VALUES
Subnormals count in steps of 1/32
The three stored fraction bits make 0.FFF₂ increase by 1/8 each time. Multiplying by the fixed 2⁻² scale makes each step 1/32. So the field value F counts steps of 1/32.
F bits value
0 000 0/32
1 001 1/32
4 100 4/32 = 1/8
7 111 7/32
Subnormal value = F/32
Ask: what is the next value after 7/32?
12 / 24
Notes: Derive the step: one fraction unit is 1/8; multiplying by 2^-2=1/4 gives 1/32. For this practice format, E=0,F=0 is zero and E=0,F=1..7 are positive subnormals. Let students answer 8/32=1/4 before the boundary slide. Source: lecture 6 subnormal equation.

## Slide 13
FLOATING POINT · WORKED EXAMPLE
Encode a subnormal: 1/8
1/8 is below the smallest normal, 1/4, so E = 0. A subnormal here is worth F/32. Solve F/32 = 1/8: F = 4, which is 100₂ in three bits.
S = 0
E = 0 = 000₂
F = 4 = 100₂
Fields: 0 | 000 | 100
Check: 4/32 = 1/8
No hidden 1: read the significand as 0.100₂.
13 / 24
Notes: Keep the calculation concrete: 1/8=4/32, so F=4. Decode using 0.100 binary times 2^-2: 1/2 times 1/4 is 1/8. Ask why E is zero and why F is four. Source: lecture 6 subnormal equation.

## Slide 14
FLOATING POINT · BOUNDARY
The next normal is one step away
The largest subnormal is 7/32. The smallest normal is 8/32. Both use the 2⁻² scale; the implied leading digit changes from 0 to 1 when E changes from 0 to 1.
E = 0, F = 111₂
0.111₂ × 2⁻² = 7/32
E = 1, F = 000₂
1.000₂ × 2⁻² = 8/32
Gap = 1/32
Subnormal values fill the space between zero and 1/4.
14 / 24
Notes: Link back to the question on the previous step table. The step from 7/32 to 8/32 is 1/32, matching the subnormal spacing. E=0 does not mean exponent −3; both values use 2^-2. Source: lecture 6 normal and subnormal equations.

## Slide 15
FLOATING POINT · PRACTICE
Your turn: decode two patterns
Use the same format: 3 exponent bits, bias 3, and 3 fraction bits.
For each pattern, classify it, find E and F, then calculate the value.
A. 0 | 010 | 100
normal or subnormal?
value = ?
B. 0 | 000 | 011
normal or subnormal?
value = ?
If E = 0, count F steps of 1/32. Otherwise use the normal rule.
15 / 24
Notes: Allow two to three minutes. A is normal: E=2,F=4, value (1+4/8)×2^-1=3/4. B is subnormal: E=0,F=3, value 3/32. Ask students to name the equation before calculating.

## Slide 16
FLOATING POINT · CHECK
Decode answers
A has E = 2, so decode a normal value. B has E = 0, so its F = 3 means three steps of 1/32.
A. 0 | 010 | 100
(1 + 4/8) × 2⁻¹ = 3/4
B. 0 | 000 | 011
F = 3 → 3/32
If the answer seems surprising, decode the same fields back into the formula.
16 / 24
Notes: Have students explain why B is not (1+3/8)×2^-3. The exponent for subnormals is fixed at 1−bias=-2, and the leading 1 is absent.

## Slide 17
FLOATING POINT · PRACTICE
Your turn: classify two ratios
Use the same practice format: 3 exponent bits, bias 3, and 3 fraction bits.
For each ratio, decide normal or subnormal, then find E and F.
A. 3/2
normal or subnormal?
E = ? F = ?
B. 3/16
normal or subnormal?
E = ? F = ?
Compare each value with the smallest normal, 1/4, before finding bits.
17 / 24
Notes: Give two minutes. Both examples are exactly representable, so no rounding rule is needed. Ask students to check results by substituting E and F into the appropriate formula.

## Slide 18
FLOATING POINT · CHECK
Practice answers
3/2 = 1.100₂ × 2⁰, so it is normal.
3/16 is below 1/4, so it is subnormal. Since value = F/32, F = 6.
A. 3/2
E = 3 = 011₂
F = 4 = 100₂
Check: (1 + 4/8) × 1 = 3/2
B. 3/16
E = 0 = 000₂
F = 6 = 110₂
Check: 6/32 = 3/16
A fraction can be exactly representable in one format and not another.
18 / 24
Notes: Do not reveal until students have tried both. Emphasize that E=0 is a category marker here, not the unbiased exponent. E=3 represents true exponent zero because bias is three.

## Slide 19
FLOATING POINT · PRECISION
Some ratios need rounding
Only eight fraction patterns fit in three bits. A ratio such as 1/3 has a repeating binary expansion and cannot be stored exactly.
The required rounding rule decides which nearby value to store.
1/3 = 1.010101…₂ × 2⁻²
Nearby values in this format:
F = 010₂ → 5/16
F = 011₂ → 11/32
Neither is exactly 1/3.
Wait for the assignment’s rounding instructions before choosing a stored result.
19 / 24
Notes: The future homework description does not specify rounding, so do not teach truncation or nearest as a required rule. Here E=1 for both nearby normals. 5/16=0.3125, 11/32=0.34375, and 1/3≈0.3333. This replaces the earlier abstract associativity slide with a representation example directly tied to the professor's stated learning goal.

## Slide 20
FLOATING POINT · SPACING
Precision changes with scale
The same three fraction bits give eight values within each normal exponent range.
When the exponent increases by one, the distance between neighboring values doubles.
E = 3 (e = 0)
F = 0 → 1 F = 1 → 9/8
step = 1/8
E = 4 (e = 1)
F = 0 → 2 F = 1 → 9/4
step = 1/4
This is why large floating point values have larger gaps.
20 / 24
Notes: For normals with fixed E, incrementing F by one changes the value by 2^(E−bias)/8. Show how this connects to the rounding slide and lecture 6’s discussion of gaps between floats.

## Slide 21
FLOATING POINT · ASSIGNMENT PREVIEW
HW3 preview: five inputs
The professor plans a program that reads a format and a nonnegative ratio. The assignment has not been posted, so treat these details as a preview.
format: exp_bits = 3
bias = 3
sig_bits = 3
value: numerator = 5
denominator = 2
Find: E (exponent), F (fraction)
The first three inputs define the format; the last two define the value.
21 / 24
Notes: Based on the professor’s preview supplied by the TA. The intended command-line inputs are exponent bits, bias, significand bits, numerator, and denominator, in that order. The output contains the exponent and significand field values. Use 5/2 as a new teaching example. The final handout may add input and rounding details.

## Slide 22
FLOATING POINT · WORKED INPUT
HW3 preview: encode 5/2
With 3 exponent bits, bias 3, and 3 fraction bits, write 5/2 as 1.010₂ × 2¹. The true exponent is 1, so E = 1 + 3 = 4. The stored fraction is 010₂, so F = 2.
Inputs: 3 3 3 5 2
E = 4 = 100₂
F = 2 = 010₂
Output: 4 2
Check: (1 + 2/8) × 2¹ = 5/2
Move the binary point before taking the stored fraction bits.
22 / 24
Notes: This example is mathematically exact and uses the planned input order. Important TA note: the supplied draft solution computes the normal significand as (numerator << sig_bits)/denominator − 2^sig_bits without scaling by 2^power_of_two. For these inputs that draft gives F=12, outside the three-bit range, rather than F=2. Do not present that draft code as a correct answer key until the normal path is fixed. Source: professor’s preview and lecture 6 normal-value equation.

## Slide 23
FLOATING POINT · METHOD
HW3 preview: choose the equation
Compare a nonzero ratio with the smallest normal, 2^(1−bias). Below that threshold, set E = 0 and use no hidden 1.
Otherwise find the true exponent e and store E = e + bias. Solve for F, then decode to check.
Normal (E > 0):
value = (1 + F/2^p) × 2^(E−bias)
Subnormal (E = 0):
value = (F/2^p) × 2^(1−bias)
If numerator = 0: E = 0, F = 0
Use the supplied p and bias, not the values from our practice format.
23 / 24
Notes: Here p is the number of significand bits. For exact examples, solve the equation algebraically. The eventual homework may specify how to round values that fall between encodings, so do not assume a rounding rule yet. This is a conceptual approach, not a copy of the unreleased source code. Source: professor’s preview and lecture 6 equations.

## Slide 24
FLOATING POINT · RECAP
How to check an encoding
In our practice format, E = 0 means count F steps of 1/32. Otherwise decode e = E − 3 and use the implied leading 1.
For an inexact value, follow the problem’s rounding rule.
Our practice format
Normal: (1 + F/8) × 2^(E−3)
Subnormal: F/32 (E = 0)
E = 0, F = 0 → zero
Decode your bits as a final check.
A correct encoding must reproduce the intended value or its required rounded value.
24 / 24
Notes: Review the two mistakes most likely to occur: forgetting to add the bias for a normal exponent, and using the normal hidden 1 for a subnormal. Do not reveal the unreleased homework solution. Remind students to follow the eventual assignment’s rounding and valid-input rules.